## Slide 1
  Bucksport Community Flood Mitigation Meeting
  Big Bull Landing Road Project
  Cowford Swamp
December 8, 2022
Horry County Government

## Slide 2
Agenda
- Introductions
- Past Flooding in Bucksport and Causes
- Flood Mitigation Project Progression
- Funding Source for the Project
- Design and Engineering Overview
- Review Recent Concerns from Public Comment
- Comments/Questions
Notes: Thom Roth Andy Markunas

## Slide 3
Bucksport
Bucksport
Notes: Thom Roth

## Slide 4
Notes: Thom Roth

## Slide 5
FEMA Flood Elevations
Waccamaw River
Pee Dee River
Cowford Swamp
Notes: Thom Roth

## Slide 6: Cowford Swamp Flow
Normal Storm Event
Riverine – Backwater Flood
Notes: Thom Roth

## Slide 7
Bucksport Area Riverine (Backwater) Flood Flows - Current
Notes: Thom Roth

## Slide 8
Bucksport Area Riverine (Backwater) Flood Flows – Proposed (after project)
Overflow channel designed to handle local storm runoff during a river flooding event only when drainage outfall under Big Bull Landing Road is closed (temporarily).
Notes: Thom Roth

## Slide 9: Grant Information
Funder: U.S. Department of Housing & Urban Development (HUD)
Program: Community Development Block Grant – Mitigation (CDBG-MIT)
State Recipient: SC Office of Resilience
Subrecipient: Horry County
Grant Funding: Big Bull Landing Road Raising: $893,750
Grant Funding: Cowford Swamp Tributary Channel: $1,582,500
Notes: Thom Roth

## Slide 10
PEE DEE RIVER AND
WACCAMAW RIVER WATERSHEDS
Notes: Waccamaw River Watershed 1/10 the size of the Pee Dee River Watershed
Rick Karkowski

## Slide 11
Normal
Flow Condition
Pee Dee River Backwater
Flooding Condition
Notes: Rick Karkowski

## Slide 12
Pee Dee River Backwater
Flooding Condition
Flow Cross Section
Project Area
Notes: Rick Karkowski

## Slide 13
Big Bull Landing Road Raising and Bucksport Relief Channel
Raise Big Bull Landing Road approximately 2700 ft long and 7-8 feet high at it’s lowest point. The entire road will not be raised, just the portion in red.
Create relief channel to allow for drainage when the crossing under Big Bull Landing is closed
Notes: Rick Karkowski

## Slide 14
Hurricane Florence
Elevation 16
Overtops Existing & Raised Road
Height
Hurricane Matthew
Elevation 13.6
Overtops Existing Road Height
Juaquin Flood Event
Elevation 10.7
Overtops Existing Road Height
Big Bull Landing Road – Flood Elevations
Big Bull (Existing)- 8.0
PIPE
Big Bull (Proposed)- 15.0
Bucksport
Notes: Rick Karkowski

## Slide 15
TS Joaquin 10.7
Big Bull (Proposed)- 15.0
Hurricane Florence - 16.1
Big Bull Landing Road – Flood Elevations
Hurricane Matthew – 13.6
Big Bull (Existing)- 8.0
PIPE
Notes: Rick Karkowski

## Slide 16
Big Bull Landing Road Without Project
PIPE
Bucksport
Notes: Rick Karkowski

## Slide 17
Big Bull Landing Road With Project
PIPE
Big Bull Landing Road
Bucksport
Protects Bucksport for Flood Event up to Elevation of 15-ft
Notes: Rick Karkowski

## Slide 18
Main Flow Area
Big Bull Landing Road
Pee Dee River Flood Flow Cross Section
At Big Bull Landing Road
120,300 sq. ft.
Ineffective Flow Area
Ineffective Flow Area
Project Area
Blocked Area
8,590 sq. ft.
Proposed Area of Fill
Notes: Slide is Hidden. To
Rick Karkowski
be used if needed.

## Slide 19
Big Bull Landing Road Improvements
Notes: Rick Karkowski

## Slide 20
Big Bull Landing Road Improvements
Local Drainage Maintained By Swales
Notes: Rick Karkowski

## Slide 21
Big Bull Landing Road Improvements
Profile
Fill
Local Drainage Maintained By Swales
Notes: Rick Karkowski

## Slide 22
Bucksport Road Relief Channel (1 of 2)
Plan
Profile
No Wetland Impacts
Invert 9.0 ft. NAVD 88
Approximately 4.0 ft. above bottom of wetland
Notes: Rick Karkowski

## Slide 23
Bucksport Road Relief Channel (2 of 2)
Plan
Profile
Existing Outfall
Location
No Wetland Impacts
Rick Karkowski
Notes: Rick Karkowski

## Slide 24
Full Cowford Swamp Watershed (12.5 sq. mi.)
Pre- and Post-Project Scenarios
Historic Hurricane Events (Rainfall / River Stages)
  Joaquin (2015)
  Matthew (2016)
  Florence (2018)
Local Rainfall Flood Events
  2-year (4.5 inches)
  10-year (6.7 inches)
  25-year (7.6 inches)
  50 year (8.6 inches)
  100-year (9.7 inches)
Engineering Analysis / Model Study
Pee Dee River Boundary
Waccamaw River Boundary
Rainfall
Notes: Rick Karkowski

## Slide 25
Notes: Hurricane Joaquim
“1000-yea flood”
Rick Karkowski

## Slide 26
Notes: Hurricane Matthew
Waccamaw River gage was damaged/did not function for a portion of the event
Rick Karkowski

## Slide 27
Notes: Hurricane Florence
Proposed project would have been overtopped
Rick Karkowski

## Slide 28
Notes: Hurricane Bertha
Did not model
Rick Karkowski

## Slide 29
Notes: Not a hurricane event – extreme rainfall in Pee Dee and Waccamaw watersheds
Did not model
Rick Karkowski

## Slide 30
Pre-Project (Existing)
2015 (H. Joaquin) Flooding Extents
Bucksport Area
Post-Project
Notes: Rick Karkowski

## Slide 31
Pre-Project (Existing)
2016 (H. Matthew) Flooding Extents
Bucksport Area
Post-Project
Notes: Rick Karkowski

## Slide 32
Pre-Project (Existing)
2021 Flooding Extents
Bucksport Area
Post-Project
Notes: Rick Karkowski

## Slide 33
Pre-Project (Existing)
2016 (H. Matthew) Flooding Extents
Little Lamb Area
Post-Project
Notes: Rick Karkowski

## Slide 34: Design Features
Addresses Pee Dee River Backwater Flooding
Only Fully Operational During Pee Dee Backwater Flood Events – Requires County Mobilization Prior to the Event
Added Big Bull Landing Culvert Capacity to Account for Potential Lost Overtopping Capacity
Bucksport Road By-Pass Channel is for Emergency By-Pass Capacity Only (Will Not Introduce Waccamaw River Flow into Cowford Swamp)
Maintain Local Drainage Patterns
Maintain Cowford Swamp Tributary Flow Patterns (Except in Pee Dee River Backwater Flooding Event)
Model Study Demonstrates No Negative Impacts North of Big Bull Landing
Will Not Alter Water Quality
Notes: Rick Karkowski